Intro
Transformers form a core part of modern technology, being used for impedance matching within electronics and electricity transmission on the grid. In both systems, the efficiency and performance are determined by how the transformer responds to an applied magnetic field. This response is described by the relationship between the magnetic flux density $B$ and the magnetising field $H$, known as the B–H curve. By altering the core of the transformer its properties can be changed. For ferromagnetic materials, the B–H curve is non-linear and exhibits hysteresis [X]. $\\$
[insert hysteresis curve] $\\$
The most efficient transformers are made by having a high magnetic susceptibility ($\mu_r$) and low energy loss per cycle. This experiment aims to quantify the usability of different materials as transformer cores. In section 2 of this report will go through the relevant theory. Then the experimental setup in section 3 followed by the results it has yielded in section 4 penultimately the analysis of these and their comparison against theoretical expectations in section 5 and finally the conclusion.

Theory
The magnetising field $H$ inside a solenoid is given by
[b = n I /L]
where n is the number of turns, i the current, and L the solenoid length.
This gives rise to the magnetic flux density $B$
For non-magnetic media there is a linear relationship:
[B=μ0​μr​H]
However, when using magnetic materials:
[B=μ0​(H+M)]
μ0 is …
μr is …

by using different materials within the centre of the solenoid different values of $mu$ are used resulting in different hysteresis loops being formed.
These B and H values cannot be measured directly. But if you arrange 2 solenoids as in [$\cref$]
[figure]
the variance of the magnetic field in one (the primary solenoid) results in an induced $emf$ in the other coil.
Given by faradays law
[ℰ𝑠 = 𝑛𝑠 𝜕phi dt]
Where
E is the emf induced in the secondary coil
N_s is the number of turns of coil
And d phi/dt s the rate of change of flux

Phi, the magnetic flux given by
[phi = B A_s ]
Where B is the magnetic field strength inside the coil and is provided by the primary coil and A_s is the area of the secondary coil.

This secondary coil then allows us to calculate phi by integrating [eqnabove] to give
B = tb calc (check 6.5 lab manual)

Then through the use of an integrator circuit we can let [I = integral..] and then measure B using
V = …

This allows us to measure our B and H through our coils and plot a hysteresis loop as the AC current changes.

Our loop allows us to calculate the…[

]